2017 Consumer Confidence Report

Town of Seabrook Water System

PWS ID# 2111010

Introduction

Like any responsible public water system, our mission is to deliver the best-quality drinking water and reliable service at the lowest, appropriate cost.  Aging infrastructure presents challenges to drinking water safety, and continuous improvement is needed to maintain the quality of life we desire for today and for the future.

In the past year, the Department completed several projects including cleaning and redeveloping Rockwells No. 2 and 4, installing video cameras at the Water Treatment Facility (WTF) and the Route 107 Pumping Station funded by the Department of Homeland Security, conducting a leak detection program on the entire water distribution system funded by the New Hampshire Department of Environmental Services (NHDES), and performing inspections on the Route 107 and Route 286 water storage facilities.   Work also continued on the ongoing two year groundwater level monitoring program and water supply exploration program.

In the coming year, we will be cleaning and redeveloping Gravel Packed Well No. 4, installing a new 8 inch water main on Anne’s Lane, completing the two year groundwater level monitoring program, and continuing the water supply testing program by exploring for more potential water supply sources.

These investments along with on-going operation and maintenance costs are supported by user rates and the tax base.  When considering the high value we place on water, it is truly a bargain to have water service that protects public health, fights fires, supports businesses and the economy, and provides us with the high-quality of life we enjoy.

What is a Consumer Confidence Report?

The Consumer

Confidence Report (CCR) details the

quality of your

drinking water, where

it comes from, and where you can get more information.  This annual report documents all detected primary and secondary drinking water parameters, and compares them to their respective standards known as Maximum Contaminant

Levels (MCLs).

The sources of drinking water (both tap water and bottled water) include rivers, lakes, streams, ponds, reservoirs, springs, and wells.  As water travels over the surface of the land or through the ground, it dissolves naturally occurring minerals and, in some cases, radioactive material, and can pick up substances resulting from the presence of animals or from human activity.

Contaminants that may be present in source water include:

Microbial contaminants, such as viruses and bacteria, which may come from sewage treatment plants, septic systems, agricultural livestock operations, and wildlife.

Inorganic contaminants, such as salts and metals, which can be naturally occurring or result from urban storm water runoff, industrial or domestic wastewater discharges, oil and gas production, mining or farming.

Pesticides and herbicides, which may come from a variety of sources such as agriculture, urban storm water runoff, and residential uses.

Organic chemical contaminants, including synthetic and volatile organic chemicals, which are by-products of industrial processes and petroleum production, and can also come from gas stations, urban storm water runoff, and septic systems.

Radioactive contaminants, which can be naturally occurring or be the result of oil and gas production and mining activities.

In order to ensure that tap water is safe to drink, EPA prescribes regulations which limit the amount of certain contaminants in water provided by public water systems.  The US Food and Drug Administration (FDA) regulations establish limits for contaminants in bottled water which must provide the same protection for public health.

What is the source of my drinking water?

The Seabrook water system is supplied by groundwater from five gravel-packed wells and seven rockwells located in the western part of town.  These wells supplied approximately 355 million gallons of water to the Town in 2016.  The gravel-packed wells range from 50 to 125 feet deep.  The rockwells are 400 to 500 feet deep.

Gravel-Packed Wells 1, 3 and 7 pump water directly into the distribution system and are chlorinated with sodium hypochlorite.  Raw water is pumped to the WTF from nine wells consisting of seven bedrock wells and two gravel-packed wells.  The WTF process includes greensand filtration for iron, manganese, and arsenic removal and bubble aeration for radon removal.  The raw water is treated with sulfuric acid which decreases the pH for optimum iron, manganese and arsenic removal.  Sodium hypochlorite promotes oxidation of iron, manganese and arsenic.  Ferric chloride absorbs oxidized arsenic.  After water passes through the pressure filters and the aeration units, sodium hypochlorite can be added to the water for disinfection.  The clearwell, a concrete basin located below the facility, stores the finished water until delivery to the water system.   At this point, operators add potassium hydroxide for final pH adjustment and optimal corrosion control for customer plumbing.

Why are contaminants in my water?    Drinking water, including bottled water, may reasonably be expected to contain at least small amounts of some contaminants.  The presence of contaminants does not necessarily indicate that water poses a health risk.  More information about contaminants and potential health effects can be obtained by calling the Environmental Protection Agency’s (EPA’s) Safe Drinking Water Hotline at 1-800-426-4791.

Do I need to take special precautions?    Some people may be more vulnerable to contaminants in drinking water than the general population. Immuno-compromised persons such as persons with cancer undergoing chemotherapy, persons who have undergone organ transplants, people with HIV/AIDS or other immune system disorders, some elderly, and infants can be particularly at risk from infections.  These people should seek advice about drinking water from their health care providers. EPA/CDC guidelines on appropriate means to lessen the risk of infection by Cryptosporidium and other microbial contaminants are available from the Safe Drinking Water Hotline at 1-800-426-4791.

Source Water Assessment Summary

DES prepared drinking water source assessment reports for all public water systems between 2000 and 2003 in an effort to assess the vulnerability of each of the state’s public water supply sources. Included in the report is a map of each source water protection area, a list of potential and known contamination sources, and a summary of available protection options.   The assessment for the wells in Seabrook was prepared on June 13, 2000 except for GPW 7 which was prepared on June 10, 2005.  These results are noted in the Source Assessment Information table.

Note: This information is over ten years old and includes information that was current at the time the report was completed.   Therefore, some of the ratings might be different if updated to reflect current information.   At the present time, DES has no plans to update this data.

| Source Assessment Information |
| --- |
| Source | Susceptibility Factors |
| Name | Low | Med | High |
| GPW 1 | 4 | 5 | 3 |
| GPW 2 | 5 | 4 | 3 |
| GPW 3 | 3 | 6 | 3 |
| GPW 4 | 4 | 5 | 3 |
| GPW 7 | 6 | 4 | 2 |
| RW 1 | 4 | 4 | 4 |
| RW 2 | 4 | 4 | 4 |
| RW 3 | 5 | 4 | 3 |
| RW 4 | 5 | 5 | 2 |
| RW 5 | 5 | 5 | 2 |

GPW – Gravel-packed well;  RW – Rockwell

The complete Assessment Report is available for review at the Water Department Office,   550 Route 107.   For more information visit the NH DES Drinking Water Source Assessment website at: http://des.nh.gov/organization/divisions/water/ dwgb/dwspp/dwsap.htm.

How can I get involved?

For more information about this report, or any questions relating to your drinking water, please call George Eaton, Primary Operator, at (603) 474-9921 or send an email to gmeaton@seabrooknh.org.  Also, the Town Manager and Selectmen can be contacted at (603) 474-3311, if additional information is required.  The Board of Selectmen/Water Commissioners meets every other Monday.

Violations and Other Information:

There were no violations.

Definitions of Table Terms and

Abbreviations

The definitions below are terms used in the

Detected Water Quality Results Table.

Action Level or AL: The concentration of a contaminant which, if exceeded, triggers treatment or other requirements which a water system must follow.

Maximum Contaminant Level or MCL: The highest level of a contaminant that is allowed in drinking water.  MCLs are set as close to the MCLGs as feasible using the best available treatment technology.

Maximum Contaminant Level Goal or MCLG: The level of a contaminant in drinking water below which there is no known or expected risk to health.  MCLGs allow for a margin of safety.

Maximum Residual Disinfectant Level or MRDL: The highest level of a disinfectant allowed in drinking water.  There is convincing evidence that addition of a disinfectant is necessary for control of microbial contaminants.

Maximum Residual Disinfectant Level Goal or MRDLG: The level of a drinking water disinfectant below which there is no known or expected risk to health.  MRDLGs do not reflect the benefits of the use of disinfectants to control microbial contaminants.

Abbreviations

ND: Not Detectable at testing limits

pCi/L: picocuries per liter

ppb: parts per billion

ppm: parts per million

ppt: parts per trillion

RAA: Running Annual Average

Sampling Results:  The results for detected contaminants listed in the table are from the most recent monitoring done in compliance with regulations ending with calendar year 2016.  The DES allows water systems to monitor for some contaminants less than once per year because concentrations of the contaminants do not change frequently.  Thus some data present, though representative, may be more than one year old.

We participated in EPA’s Unregulated Contaminant Monitoring Rule (UCMR3) program in 2013 and 2016.  Unregulated contaminants are those that don’t yet have a drinking water standard set by the EPA.  The purpose of monitoring for these contaminants is to help EPA decide whether the

contaminants should have a standard.

| DETECTED WATER QUALITY RESULTS |
| --- |
| Inorganic Contaminants | Units | MCL | MCLG | Max Level Detected | Range | Violation Yes/No | Likely Source |
| Barium (2015) | ppm | 2 | 2 | 0.0278 | 0.0177-0.0278 | No | Erosion of natural deposits |
| Nitrate (as Nitrogen) | ppm | 10 | 10 | 1.07 | ND-1.07 | No | Runoff from fertilizer use; Leaching from septic tanks, sewage; Erosion of natural deposits |
| Inorganic Contaminants | Unts | MCL | Date | 90th Percentile | # of Sites Above AL | Violation Yes/No | Likely Source |
| Copper | ppm | AL=1.3 | 3/2016 & 4/2016 | 0.61 | 0 of 60 sites | No | Corrosion of household plumbing systems |
| Lead | ppb | AL=15 | 3/2016 & 4/2016 | 2.3 | 0 of 60 sites | No | Corrosion of household plumbing systems |
| Radioactive Contaminants | Units | MCL | MCLG | Average Amount | Range | Violation Yes/No | Likely Source |
| Uranium | ppb | 30 | NA | 0.4 | ND-1.3 | No | Erosion of natural deposits |
| Combined Radium (226+228) | pCi/L | 5 | 0 | 2.3 | 1-4 | No | Erosion of natural deposits |
| Volatile Organic Contaminants | Units | MCL | MCLG | Amount Detected | Range | Violation Yes/No | Likely Source |
| Haloacetic Acids (HAA5s) | ppb | 60 | NA | 6.5 | 4.3-6.5 | No | By-product of chlorination |
| Total Trihalomethanes (TTHMs) | ppb | 80 | NA | 33 | 18-33 | No | By-product of chlorination |
| Disinfectant | Units | MRDL | MRDLG | RAA | Range | Violation Yes/No | Likely Source |
| Chlorine | ppm | 4 | 4 | 0.43 | 0.14-0.84 | No | Water additive used to control microbes |
| Unregulated Contaminant Monitoring (UCMR3) | Units | Average Amount | Range | Likely Source |
| Chlorate (2013) | ppb | 74.5 | ND-184 | Agricultural defoliant or desiccant; disinfection by-product; used in production of chlorine dioxide |
| Hexavalent Chromium (2013) | ppb | 0.064 | ND-0.11 | Erosion of natural deposits; discharges from steel and pulp mills |
| Chromium, Total (2013) | ppb | 0.27 | ND-0.48 | Used in making stainless steel, dyes, leather tanning, anti-corrosion coatings |
| Strontium, Total (2013) | ppb | 179 | 135-244 | Naturally occurring element; was used in face plating glass of cathode-ray tubes |
| Perfluorooctanoic Acid (PFOA) | ppt | 6.0 | ND-14 | Used for its emulsifier and surfactant properties in or as fluoropolymers (such as Teflon), fire-fighting foams, cleaners, cosmetics, greases and lubricants, paints, polishes, adhesives and photographic films |
| Perfluorooctane Sulfonate Acid (PFOS) | ppt | 1.8 | ND-6.7 | Surfactant or emulsifier; used in fire-fighting foam, circuit board etchings acids, alkaline cleaners, floor polish, active ingredient in insect bait traps; U.S. manufacture of PFOS phased out in 2002 although PFOS still generated accidentally. |